Author: Rik Starmans
Title: Notes for firestarter design
Abstract: Notes that were made while designing the Firestarter.

Screen:
There are several options for adding a screen.
   I2C protocol 4D Systems 80 euro, but is too invasive and requires a CAPE.
    Geekcreit 7 inch or 5 inch hdmi around 50 euro, requires HDMI and USB.
   Manga Screen (kickstarter, elias bakken, 90 euro)

You want the ability to add a HDMI screen later. So do not use P8 pin 27 up to 46 and pin 9.28, 9.29 and 9.31, see link.

Stepper driver:
Stepper driver, you use the TMC. It is described here. You need an SPI port. You can only use SPI0 as the SPI1 is taken by HDMI, which implies 9.17, 9.18, 21 and 22.
Yes, a separate slave select per slave with the other signals in common is correct. You can daisy-chain with TMC2130. If more than 40 clocks are driven, the additional bits shifted into SDI are shifted out on SDO after a 40-clock delay through an internal shift register. However, this was not used.
P9_22 (SPI0_SCLK => SCLK) outputs a serial clock signal to synchronize communications. P9_18 (SPI0_D1 => MOSI) outputs data to the SPI peripheral device.
P9_21 (SPIO_DO => MISO) receives data from the SPI peripheral device.
P9_17 (SPI0_CSO => CE0) enables one SPI peripheral device.

Digipot
For the Digipot you need I2C. You can’t use I2C1 as it requires 17 which is used for TMC. You can use I2C2 as it requires
19, 20.

Laser Extension board;
You contemplated on a laser extension board which could be hooked via a data cable. On a data cable, the red wire signals pin 1.
You would need at least the following pins
laserpin 1 (IC HB PWM1)
      laserpin 2 (IC HB PWM2)
      photodiode
       potw (power laserdiode)
The point is it is not needed at the moment, you want the simplest design possible.

Motor cables:
AWG < AWG 17 around 1.7A max per NEMA 17 so total 3A

Expected currents:

Motor circuit
Nema 17 motor uses 1.7A at 12V, spindle (DC 775 motor) uses up to 25A. Typically, spindle uses 12A.
The safety circuit for the spindle does not handle this current.
Laser circuit
The driver can supply up to 300 mA.

Safety Circuit
The safety procedure is outlined here. You start with a hazard identification. You then determine the measures and how they should be implemented (minimum category), see omron.
The motor circuit and laser should be separate. You can then break the motor with an e-stop and the laser with a magnetic interlock. The machine cannot immediately start if the e-stop is closed.
The following is circuit is used to reactivate the circuit with a start button, see safety relay. The problem with any semiconductor device in a safety critical circuit is predicting failure modes, in general you can't. That’s why it can’t be used in a safety circuit. There are however solid-state relays for hazardous situations. I don’t know how they compare with force guided contacts.
If you design a safety guard, you should also take into account the distance to the hazard and how the guard opens.
Besides the regulation you can also look at similar hardware, a tear down of the Form 2 can be found here . The company also hosts interactive 3D teardowns. Formlabs uses a magnetic interlock. It does not seem to be using any relays. Due to the limited budget and as we r designing MVP.

Spindle control / Stepper motors
Add a e-stop which disables power to the motors by holding the reset pin low on the PSU.
The e-stop is more of a power button and does not include a start button. If the e-stop is de-actived the system powers on.
Laser Safety:
Use a an upward flip like Formlabs and a a magnetic interlock. Add a button so you can see whether power is supplied to the laser and turn it of or on.

Safety Switch:
MC1 440N Magnetic Safety Switch, Plastic (38.20 euro) uses reed contact so should work with lower voltages.

Spindle control
The spindle can be controlled via PWM. You can use a transistor or a MOSFET to PWM the spindle.

Transistor
A simple circuit can be found here. Calculations need to be made to select the correct NPN transistor are here. A PNP transistor should not be selected as it can only handle the same voltage. Motor is 150W at 12V, can draw at least 12A on video seems to be able to draw up to 25A. The amplifier is at least 750 so for 20.000 mA/750 = 27 mA.
Voltage drop can vary between from 3.3V to 1V or 2V. They resistor becomes than 2.3V/25mA=91 Ohm. Smaller might be required in some cases but could lead to trouble.
Looking at the result we select the following MJH6284G (NPN).
An alternative is this PMD16K80. It can amplify more but does not look to be in a correct casing.
Transistors require a heatsink. The power you want to dissipate is P=VI and most dominated by the collector voltage so P=12*10 (worst case). However, if you read the doc you see the Collector-Emitter saturation voltage is like 2 or 3V. So the power is 3*20=60 Watt (worst case).
For high current applications you can better use a MOSFET.

MOSFET
The IRLB8721PbF can be used up to 15A without cooling. The threshold voltage is 2.5V, see details.
Use a 10 kOhm resistor to prevent a floating pin. You connect the PWM pin to the gate. The source to the ground and the drain to the negative pole of the motor. Schottky diodes are preferred in fly-back application because they have the lowest voltage drop
You need to PWM at least at 20kHz to prevent audible sound. The STPS1545D seems good enough.

Literature

The following information was also collected during the write up of the document.
Other 3D printer controller boards:
    DUET
    SMOOTHIE
   REPLICAPE / REVOLVE (uses PRU); basically you can get the octavo; a beaglebone in a bga
   RAMBO

If you want to bring it to a single board you can use the OSD3358 (octavo chip). This also forms the basis for the beaglebone pocket.

height sensor https://www.duet3d.com/DuetAddons/IRProbe (IR probe)