Stepper driver, you use the TMC. It is described here.

You configure the motor via:

Pins:
  SDCO
 CS
 SCK
  SDI

It used to be pins and MS1,2,3 and jumpers (which has been replaced)

You control the motor via:
  STEP
 DIR
 ENABLE

op het bord:
  POT SDA (voor ADC)
  POT SCL

datakabel gebruiken is meer pro, bij stepper en endstops doe je dat niet. Dit komt meer door gewoonte.

pins nodig:
 5V
  3V
  laserpin 1 (IC HB PWM1)
 laserpin 2 (IC HB PWM2)
 photodiode
  potw (power laserdiode)
  ZPO (endstop switch)
  4 kabels voor motor (configuratie)
  2 kabels voor motor control

Motor cables:
AWG < AWG 17 around 1.7A max per NEMA 17 so total 3A

Merk op rode geeft pin 1 aan, hoeft niet meteen stroom te zijn.

Total current:
Nema 17 motor uses 1.7A at 12V, spindle (DC 775 motor) use up to 25A. Typically, spindle uses 12A.
The safety circuit for the spindle does not handle this current.

Safety Circuit
A tear down of the Form 2 can be found here . The company also hosts interactive 3D teardowns.
Formlabs uses a magnetic interlock. It does not seem to be using any relays.
You have thought of using a forcibly guided contact in combination with a contactor or a solid-state relay. The problem with any semiconductor device in a safety critical circuit is predicting failure modes, in general you can't. That’s why it can’t be used ina safety circuit.

Category your system is in.
Read out high voltage;
https://forum.arduino.cc/index.php?topic=425112.0

Safety Switch:
MC1 440N Magnetic Safety Switch, Plastic (38.20 euro) uses reed contact so should work with lower voltages.

Spindle control
The spindle can be controlled via PWM. You can use a transistor or a MOSFET to PWM the spindle.

Transistor
A simple circuit can be found here. Calculations need to be made to select the correct NPN transistor are here. A PNP transistor should not be selected as it can only handle the same voltage. Motor is 150W at 12V, can draw at least 12A on video seems to be able to draw up to 25A. The amplifier is at least 750 so for 20.000 mA/750 = 27 mA.
Voltage drop can vary between from 3.3V to 1V or 2V. They resistor becomes than 2.3V/25mA=91 Ohm. Smaller might be required in some cases but could lead to trouble.
Looking at the result we select the following MJH6284G (NPN).
An alternative is this PMD16K80. It can amplify more but does not look to be in a correct casing.
Transistors require a heatsink. The power you want to dissipate is P=VI and most dominated by the collector voltage so P=12*10 (worst case). However, if you read the doc you see the Collector-Emitter saturation voltage is like 2 or 3V. So the power is 3*20=60 Watt (worst case).

For high current applications you can better use a MOSFET.
The challenge with MOSFET is that they are voltage controlled.

MOSFET
FET; https://electronics.stackexchange.com/questions/322522/high-voltage-pwm-motor-controller-mosfets-explode

Literature
Other 3D printer controller boards:
    DUET
    SMOOTHIE
   REPLICAPE / REVOLVE (uses PRU); basically you can get the ottavo; a beaglebone in a bga
   RAMBO

If you want to bring it to a single board you can use the OSD3358 (octavo chip). This also forms the basis for the beaglebone pocket.

height sensor

sell ir probe (could be nice)
https://www.duet3d.com/DuetAddons/IRProbe