Stepper driver, you use the TMC. It is described here.

You configure the motor via:

Pins:
  SDCO
 CS
 SCK
  SDI

It used to be pins and MS1,2,3 and jumpers (which has been replaced)

You control the motor via:
  STEP
 DIR
 ENABLE

op het bord:
  POT SDA (voor ADC)
  POT SCL

datakabel gebruiken is meer pro, bij stepper en endstops doe je dat niet. Dit komt meer door gewoonte.

pins nodig:
 5V
  3V
  laserpin 1 (IC HB PWM1)
 laserpin 2 (IC HB PWM2)
 photodiode
  potw (power laserdiode)
  ZPO (endstop switch)
  4 kabels voor motor (configuratie)
  2 kabels voor motor control

Motor cables:
AWG < AWG 17 around 1.7A max per NEMA 17 so total 3A

Merk op rode geeft pin 1 aan, hoeft niet meteen stroom te zijn.

Total current:
Nema 17 motor uses 1.7A at 12V, spindle (DC 775 motor) uses 2.6A.
Total = 1.7A*3+2.6A=7.7A

Safety Circuit
A tear down of the Form 2 can be found here . The company also hosts interactive 3D teardowns.
Formlabs uses a magnetic interlock. It does not seem to be using any relays.
Read out high voltage;
https://forum.arduino.cc/index.php?topic=425112.0

Safety Switch:
MC1 440N Magnetic Safety Switch, Plastic (38.20 euro) uses reed contact so should work with lower voltages.

Spindle control
The spindle can be controlled via PWM. A simple circuit can be found here.

Literature
Other 3D printer controller boards:
    DUET
    SMOOTHIE
   REPLICAPE / REVOLVE (uses PRU); basically you can get the ottavo; a beaglebone in a bga
   RAMBO

If you want to bring it to a single board you can use the OSD3358 (octavo chip). This also forms the basis for the beaglebone pocket.

height sensor

sell ir probe (could be nice)
https://www.duet3d.com/DuetAddons/IRProbe